###### General Permit #1

###### Stormwater Pollution Prevention Plan

(Facility)

(Date)

###### TABLE OF CONTENTS

## General Facility Information

Introduction & Objectives

##### Phase1:  Planning and Organization

Storm Water Pollution Prevention Team

##### Existing Environmental Management Plans

## Phase 2:  Assessment

Assessment of Potential Sources of Storm Water Pollution and Site Map

Figure 1:  Site Map

Inventory of Significant Material and Exposure Information

List of Past Spills/Leaks and Hazardous Condition

Non-Storm Water Discharge Assessment

Non-Storm Water Discharge Assessment Certification

Failure to Certify Non-Storm Water Discharges

Non-Storm Water Discharge Assessment Failure to Certify Notification

Existing Monitoring Data

Site Evaluation Summary

Phase 3 & 4:  Best Management Practice Selection, Implementation, Employee Training.

Best Management Practices: Summary and Schedule of Implementation

Good Housekeeping

Preventative Maintenance

Visual Inspection

Spill Prevention and Response Plan

Sediment and Erosion Prevention

Runoff Control – Diversions

Runoff Control – Containment

Other Controls

BMPs from Site Evaluation

Employee Training

## Phase 5 & 6:  Evaluation

Record Keeping, Internal Report and Annual Report

Site Evaluation

Annual Site Compliance Evaluation

Record Keeping and Reporting Forms

Annual Report

## Phase 7: General and Special Requirements

General Requirements

Certification Statement

Special Requirements

Appendix A:  Inspection and Reporting Forms

Appendix B:  List of Tables

###### GENERAL FACILITY INFORMATION

Name of Facility:

Facility Address:

Owner:

Facility Contact:

Name:

Title:

Telephone:

Mailing Address:

Standard Industrial classification (SIC) Code:

Permit Information:

Type:  General Permit No. 1

Permit Number:

Effective Dates of Coverage:

Number of Storm Water Outfalls:

Receiving Waters:

Outstanding Iowa Waters :       (name if applicable)

Outstanding National Resource Waters:        (name if applicable)

Emergency Contact:

Name:

Telephone:

INTRODUCTION & OBJECTIVES

This storm water pollution prevention plan (SWPPP) covers the operations at

.  (facility name)

It has been developed as required under Iowa’s National Pollutant Discharge Elimination System (NPDES) General Permit for storm water discharges.  This SWPPP describes facility operations, identifies potential sources of storm water pollution at the facility, lists best management practices (BMPs) or pollution control measures to reduce the discharge of pollutants in storm water runoff, and provides for periodic review of this SWPPP.

The goal of the storm water permit program is to improve the quality of surface waters by reducing the amount of pollutants potentially contained in the storm water runoff being discharged.  Industrial facilities subject to an NPDES permit must prepare and implement a SWPPP for their facility.

The objective of this SWPPP is three-fold:

- Identify potential sources of pollution at the facility.

- Describe best management practices (BMPs) consistent with BMPs for the facility.

- Provide other elements such as, but not limited to, a facility inspection program, site compliance evaluation program, record keeping and reporting program that will help the facility comply with the terms and conditions of their storm water discharge permit.

## PHASE 1:  PLANNING AND ORGANIZATION

## STORM WATER POLLUTION PREVENTION TEAM

The storm water pollution prevention team is responsible for developing, implementing, maintaining, and revising this SWPPP.  The members of the team are familiar with management and operations of the facility and have used worksheets to assist them in developing this SWPPP.  Worksheets can be found with the SWPPP.

The members of the team and their primary responsibilities (i.e. implementing, maintaining, record keeping, submitting reports, conducting inspections, employee training, conducting the annual compliance evaluation, testing for non-storm water discharges, signing the required certifications) are listed  below.

| Table 1: Storm Water Pollution Prevention Team (use Worksheet –Table 1). |
| --- |
| Name & Title | Responsibility |

Note:  Add rows as needed.

EXISTING ENVIROMENTAL MANAGEMENT PLANS

(facility name)

(Choose one)

Is not required to comply with other environmental plans

Or

Is required to comply with other environmental plans, these include:

(e.g., SPCC, RMP, etc.)

PHASE 2:  ASSESSMENT

ASSESSMENT OF POTENTIAL SOURCES OF POLLUTANTS AND SITE MAP

Figure 1 presents a site map of the facility showing the following features:

- An outline of the drainage area of each storm water outfall including:

  - Drainage patterns

  - Direction of flow

  - Discharge points (outfalls)

- Existing structural storm water pollution control measures (physically constructed features used to control storm water flows), such as:

  - Flow diversion structures

  - Retention / detention ponds

  - Vegetative swales

  - Sediment traps

- Name of receiving waters (or if through a Municipal Separate Storm Sewer System)

- Location and name of surface water bodies, including any neighboring stream, river, lake or water body receiving storm water discharges from the site.

- Locations of “significant materials1 ” exposed to storm water.

- Locations of past spills and leaks (during the past three years)

- Locations for each of the following activities (where exposed to storm water):

  - Fueling stations

  - Vehicle/equipment washing and maintenance areas

  - Areas for unloading and loading materials

  - Aboveground tanks for liquid storage

  - Industrial waste management areas (landfills, waste piles, treatment plants, disposal area)

  - Outside storage areas for raw materials, by products, and finished products

  - Outside manufacturing or processing areas

  - Other areas of concern (specify: ________)

1  “significant materials” are defined in the guidance document  as:  Raw materials, fuels, materials such as solvents, detergents, and plastic pellets, finished materials such as metallic products, raw materials used in food processing or production,  hazardous substances designed under Section 101(14) of CERCLA, any chemical the facility is required to report pursuant to EPCRA Section 313,  fertilizers, pesticides and waste products such as ashes, slag and sludge that have the potential to be released with storm water discharges.

FIGURE 1.  SITE MAP (use Worksheet – Developing a Site Map)

SIGNIFICANT MATERIALS INVENTORY AND EXPOSURE INFORMATION

Table 2 is an inventory of “significant materials1” on site.  For each significant material on site an evaluation will be conducted to determine the potential for these materials to be contributed to storm water runoff being discharged from the facility.

| Table 2: Material Inventory (use worksheet - Table 2) |
| --- |
| “Significant Materials1” | Location (on site map) | Quantity (units) | Exposed in past 3 years? (yes/no) |
|  |  | Used | Produced | Discharged |  |

Note:  Add rows as needed.

Table 3 provides additional information regarding  spills or leaks of  “significant materials1 ” over the three years prior to the completion of the plan.  The date, volume of materials, the exact location of each release, and the actions taken to clean up the materials and/or prevent exposure of the materials to storm water runoff is included in addition to indicating if a “hazardous condition2” occurred.

2  “hazardous condition” is defined in the guidance:   ‘… any substance or mixture of substances that presents  a danger to the public health or safety and includes but is not limited to a substance that is toxic, corrosive or flammable, that is an irritant or that, in confinement, generates pressure through decomposition, heat or other means.  Examples:  acids, alkalis, explosives, fertilizers, heavy metals such as chromium, arsenic, mercury, lead and cadmium, industrial chemicals, paint thinners, pesticides, petroleum products, poisons, radioactive materials, sludge  and organic solvents, any substance identified by EPA  under RCRA or any toxic pollutant  listed under Section 307 of WPCA  or any DOT designated hazardous material.

| Table 3: Exposed “Significant Materials” & “Hazardous Condition” (use worksheet - Table #3) |
| --- |
| “Significant Materials1” | Date & Length of Exposure | Volume Exposed | Location (on site map) | Storage/Disposal Method | Action Taken (prevention, clean up) | “Hazardous Condition2” (yes/no) |
|  |  |  |  |  |  | I |

Note:  Add rows as needed.

More details of spills and leaks that resulted in a “hazardous condition” are found in Table 4.

| Table 4: History Of “Hazardous Condition”(use worksheet – Table 4) |
| --- |
| Date | Material | Location (on site map) | Reason for Spill/Leak | Actions to Prevent Recurrence |

Note:  Add rows as needed.

NON – STORM WATER DISCHARGE ASSESSMENT

The permit requires that all discharge locations be evaluated for the presence of non-storm water discharges.  Examples of non-stormwater discharges that may require coverage under a NPDES permit include any water used directly in the manufacturing process (process water) and vehicle or equipment washing where detergent is used.  Allowable non-stormwater discharges include:  uncontaminated ground water discharge, foundation or footing drains where flows are not contaminated with process materials, discharges from springs, routine exterior building wash down which does not use detergents or other compounds, air conditioning condensate, non-contact cooling water, pavement wash waters where spills or leaks or hazardous materials have not occurred and where detergents are not used.  Also, discharges from fire fighting activities, fire hydrant flushing, potable water sources including waterline flushing, irrigation drainage, and lawn watering are allowed.

Any unauthorized storm water discharges will be eliminated, or covered under another National Pollutant Discharge Elimination System (NPDES) permit.  Table 5 summarizes the evaluation results.

| Table 5: Non-Storm Water Discharge Assessment (use worksheet –Table 5) |
| --- |
| Date | Outfall | Method Used | Location or Source | Person Evaluating | Result of assessment and potential significant sources |

Note:  Add rows as needed.

NON-STORM WATER DISCHARGE ASSESSMENT AND CERTIFICATION

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to ensure that qualified personnel properly gather and evaluate the information submitted.  Based on my inquiry of the person or persons who manage the system or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate and complete.  I am aware that there are significant penalties for submitting false information, including the possibility of fine or imprisonment for knowing violations and that such notification will be kept on site and made available to the IDNR anytime, after 180 days from the discharge authorization date, if non-stormwater certification cannot be provided.

Name								Official Title

Area Code & Phone Number					Date

Signature

If it is not feasible to test or evaluate an outfall within 180 days of the discharge authorization date it will be noted in Table 5 below.

| Table 6: Failure to Certify Non-Storm Water Discharges (use worksheet – Table 6) |
| --- |
| Outfall Not Tested/ Evaluated | Describe Why Certification Is Not Feasible | Describe Potential Sources of Non-Storm Water Pollution |

Note:  Add rows as needed.

NON-STORM WATER DISCHARGE ASSESSMENT AND  FAILURE TO CERTIFY NOTIFICATION

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to ensure that qualified personnel properly gather and evaluate the information submitted.  Based on my inquiry of the person or persons who manage the system or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate and complete.  I am aware that there are significant penalties for submitting false information, including the possibility of fine or imprisonment for knowing violations and that such notification will be kept on site and made available to the IDNR anytime, after 180 days from the discharge authorization date, if non-stormwater certification cannot be provided.

Name		 						Official Title

Area Code & Phone Number					Date

Signature

EXISTING MONITORING DATA

Storm water discharge  monitoring has not been required at this facility previously, therefore, no data exists, nor will any be collected.

However, if monitoring is required in the future, we will complete the monitoring as directed by the permit and will maintain a copy of the monitoring results with this SWPPP.

SITE EVALUATION SUMMARY

This is a narrative description of activities with a high potential to contaminate storm water at

the facility.  It includes areas, activities and materials associated with loading, unloading, outdoor storage, outdoor manufacturing or processing, onsite waste disposal and significant dust or particulate generating activities.  The information found in Table 7 is used to select the most appropriate Best Management Practices (BMPs) to prevent or control pollutants from these areas.

| Table 7: Site Evaluation Summary (use worksheet – Table 7) |
| --- |
| Activity/Area | Pollutant | Where From | Existing BMP | New BMP Options |
| Loading and Unloading Operations |  |  |  |  |
| Maintenances & Equipment Cleaning |  |  |  |  |
| Outdoor Storage Operations |  |  |  |  |
| On-Site Practices |  |  |  |  |
| Dust or Particulate Generating Processes |  |  |  |  |
| Above Ground Liquid Storage Tank |  |  |  |  |
| Outdoor Processes or Manufacturing |  |  |  |  |
| Other |  |  |  |  |

Note:  Add rows as needed.

PHASE 3 & 4:  BEST MANAGEMENT PRACTICE SLECTION, IMPLEMENTATION AND EMPLOYEE TRAINING

BEST MANAGEMENT PRACTICES:  SUMMARY AND SCHEDULE OF IMPLEMENTATION

Based on information recorded in Table7, Site Evaluation Summary, storm water management controls or best management practices (BMPs), have been or will be implemented to reduce the amount of pollutants in storm water discharge.

Non-structural controls are practices that are specifically intended to reduce the amount of pollution getting into surface waters.  They are generally implemented to address the problem at the source.  They do not require any structural changes to the facility.

Structural control measures may be necessary to control any pollutants that are still present in the storm water after the non-structural controls have been implemented.  These types of controls are physical features that control and prevent storm water pollution.  They can range from preventive measures to collection structures to treatment systems.  Structural controls will require construction of a physical feature or barrier.

The following BMP’s are a mixture of non-structural and structural control chosen for implementation at the facility.

BMP - GOOD HOUSEKEEPING

Good housekeeping practices are designed to maintain a clean and orderly work environment.  This will reduce the potential for significant materials to come in contact with storm water.

Table 8 lists good housekeeping practices that are or will be implemented, a schedule for implementation and the person responsible.

| Table 8: BMP - Good Housekeeping Practices (use worksheet Table 8) |
| --- |
| Area / Equipment | Task | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

BMP - PREVENTIVE MAINTENANCE

Preventive Maintenance involves the regular inspection, testing, and cleaning of facility equipment and operational systems.  Preventative maintenance will help to uncover conditions that might lead to a release of materials.

Table 9 contains the equipment and activities to be included in a preventive maintenance program.

| Table 9: Preventive Maintenance (use worksheet – Table 9) |
| --- |
| Equipment / Activity | Task | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

BMP - VISUAL INSPECTION

Visual inspection of the facility (equipment, plant areas, and structural controls) is required by the permit.  These inspections will occur at least once each year and after major storm events as prudent.  Records of the inspections will be kept on file with the SWPPP for a minimum of three years.  Pollution Prevention Plans will be revised after the inspection as needed.  Table 10 is a description of the visual inspection and annual schedule.

| Table 10: Visual Inspection (use worksheet – Table10) |
| --- |
| Location, Area or Equipment | Annual Inspection Date | Responsible Person | Management Practice/Method | Effectiveness (Yes/No) | Revision Notes |

Note:  Add rows as needed.

BMP - SPILL PREVENTION AND RESPONSE PLAN

Spills and leaks together are the largest industrial source of storm water pollution.  Thus, this SWPPP specifies material handling procedures and storage requirements for significant materials.  Equipment and procedures necessary for cleaning up spills and preventing the spilled material from being discharged have also been identified.  Appropriate employees have been trained to follow SWPPP procedures.

Table 11 lists procedures that have been developed for spill response at the facility, the area(s) covered, response plan location and responsible person are also included.

| Table 11: Spill Prevention And Response (use worksheet – Table11) |
| --- |
| Area Activity Equipment | Pollutant(s) of Concern | Description of Response Plan | Location of Plan and Clean up Materials/Kits | Responsible Person or Team |

Note:  Add rows as needed.

BMP - SEDIMENT AND EROSION CONTROL

There may be certain areas at the facility that are prone to soil erosion.  These areas need to be protected, and soil kept out of the storm water discharge.  If there are no areas prone to soil erosion it will be stated in this.

| Table 12. Sediment And Erosion Control (use worksheet – Table12) |
| --- |
| Area of Concern | Control Measures | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

BMP - RUNOFF CONTROL - DIVERSION PRACTICES

Diversion practices are structures (including grading and paving) that are used to divert storm water away from high-risk areas and prevent contaminants from mixing with the runoff and/or to channel contaminated storm water to a treatment facility or containment area.

Table 13 includes information on diversion practices at the facility.

| Table 13: Runoff Control – Diversion Practices (use worksheet – Table13) |
| --- |
| Area | Pollutant(s) of Concern | Diversion Measure | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

BMP - RUNOFF CONTROL - CONTAINMENT

Containment areas are structures designed to hold pollutants or contaminated storm water to prevent it from being discharged to surface waters.  These structures can range from drip pans to large containment areas required for Spill Control and Countermeasures (SPCC) plans such as secondary containment structures or detention, retention and collection basins.

Table 14 includes a list of containment measures that are currently in place or that will be implemented.

| Table 14: Runoff Control – Containment (use worksheet – Table14) |
| --- |
| Area | Pollutant(s) of Concern | Containment Measure | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

BMP - OTHER CONTROLS

There are other control measures that are used that may not fit into one of the previously mentioned categories such as, sumps, oil/water separators, sand filters, etc.  Those controls are found in Table 15.

| Table 15: Other Controls (use worksheet – Table15) |
| --- |
| Area | Material | Control Measure | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

BMP -  FROM SITE EVALUATION

Table 16 includes BMP’s that will be implemented based on information obtained during the comprehensive site evaluation conducted during an earlier activity of this plan.

| Table 16: BMP’s From Site Evaluation (use worksheet – Table16) |
| --- |
| Area / Activity | Pollutant of Concern | BMP Control Measure | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

BMP - EMPLOYEE TRAINING

An employee training program will be implemented to inform appropriate personnel at all levels of responsibility of the components and goals of this SWPPP. The more knowledgeable employees are about the facility’s SWPPP and what is expected of them, the greater the chance that the plan will be successful.  Table 17 details the training program.

| Table 17: Employee Training Program (use worksheet – Table17) |
| --- |
| Training/Information Topic | Employees Trained | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

PHASE 5 & 6:  eVALUATION

Record Keeping, Internal Report AND ANNUAL REPORT

The permit requires that records of all preventive maintenance, comprehensive visual site inspections, records of employee training sessions, records of monitoring information, and the annual report be retained at the facility for at least three years after the permit coverage expires.  Monitoring results should be retained for five years.

These records are available, upon request, to a representative of  IDNR  (within 3 days) and/or a municipal separate storm sewer system operator as appropriate.

SITE EVALUATION

Qualified personnel will conduct site compliance evaluations once each calendar year.

ANNUAL SITE COMPLIANCE EVALUATION

The following areas, management practices, activities and BMPs listed in Table 18 will be included in the annual compliance evaluation.

| Table 18: Annual Site Compliance Evaluation |
| --- |
| Area, Location, and or BMP | Effectiveness of Measures | Revision to SWPP Needed (yes/no) | Implementation Schedule | Responsible Person |

Note:  Add rows as needed.

RECORD KEEPING AND REPORTING FORMS

Forms used to conduct inspections/evaluations and report results are found in Appendix A.

ANNUAL REPORT

An annual report discussing the effectiveness of the SWPPP will be written.  This report will include any changes that have been made, the reason for the changes, any spills that occurred, what actions were taken as result of the spill, inspection results, and any other information relevant to the SWPPP.  The annual report will be retained on site with the SWPPP.

PHASE 7:  GENERAL AND SPECIAL REQUIREMENTS

GENERAL REQUIREMENTS

All Notices of Intent, SWPPP’s, reports, certifications, or information submitted to the IDNR, or the operator of a large or medium municipal separate storm sewer system will be signed by the “authorized representative” who is the person at or near the top of the facility  management chain and who has been delegated the authority to sign and certify this type of document.

The SWPPP will be located at the facility and made public as appropriate.

SPECIAL REQUIREMENTS

- (facility name) (choose one):
does or 
does not 
discharge stormwater through a Municipal Separate Storm Sewer System in a city with a population of 100,000 or more.  Relevant information outlining compliance with the MS4 special requirements is included as Attachment 1 of this SWPPP.

- (facility name) (choose one):
does or 
does not

store, handle process or transfer SARA Title III, Section 313 Water Priority Chemicals. Relevant information outlining compliance with SARA Title III special requirements is included as Attachment 2 of this SWPPP.

- (facility name) (choose one):
does or 
does not 
have salt storage piles used for deicing or other commercials purposes.  Relevant information outlining compliance with salt storage piles special requirements is included as Attachment 3 of this SWPPP.

CERTIFICATION OF THE SWPPP

I certify under penalty of law that this SWPPP has been developed in accordance with good engineering practices.  To the best of my knowledge and belief, the information submitted is true, accurate, and complete.  And at the time this plan was completed no unauthorized discharges were present.  I am aware that there are significant penalties for submitting false information, including the possibility of fine or imprisonment for knowing violations.

Name		 						Official Title

Area Code & Phone Number					Date

Signature

APPENDIX A

INSPECTION AND REPORTING FORMS

SIGNIFICANT SPILL REPORT FORM

Date of Occurrence:

Discovered by Whom:

Location:

Material Type & Volume:

Cause of Spill:

Corrective Action Taken:

Agencies/Persons Contacted:

Signature

NON-STORM WATER INSPECTION REPORT FORM

Date of Inspection:     		Time:

Inspected by (printed name):

Signature: ____________________________________________________________

Description of type of inspection (check those that apply):

- visual observation

- dye tests

- smoke tests

- TV line survey

- analysis of accurate schematics

- sampling/monitoring

- other (specify)

Observations/Results:

Are there any non-storm water discharges?

- yes

- no

Is the discharge authorized under this permit?

- yes

- no

Is the discharge covered under another National Pollutant Discharge Elimination System (NPDES) permit?

- Yes

- no

EMPLOYEE TRAINING RECORD

Date of Session:     		Time:

Trainer:     	 			Topic

****************************************************************************

Employees Attending (names, printed):		Signature:

__________________________________

________________________________

________________________________

________________________________

________________________________

________________________________

________________________________

________________________________

________________________________

________________________________

Specifics of Training:

GOOD HOUSEKEEPING INSPECTION FORM

Date:      			Time:

Inspected by:

Signature:

| Areas Inspected | Observations | Actions Taken |
| --- | --- | --- |

PREVENTIVE MAINTENANCE INSPECTION FORM

Date:     			Time:

Inspected by:

Signature: __________________________

| Areas/Equipment Inspected | Observations | Actions Taken |
| --- | --- | --- |

VISUAL INSPECTION FORM

Date:     		Time:

Inspected by:

Signature: ________________________

| Area/Equipment/BMP Inspected | Observations | Actions Taken |
| --- | --- | --- |

ANNUAL SITE COMPLIANCE EVALUATION FORM

Date:     		Time:

Conducted by:

Signature: _________________________________

| Area/Equipment/BMP Inspected | Observations | Actions Taken |
| --- | --- | --- |

APPENDIX B

LIST OF TABLES

# Table 1:  Storm Water Pollution Prevention Team

# Table 2:  Material Inventory

# Table 3:  Exposed “Significant Materials” & “Hazardous Condition”

# Table 4:  History of “Hazardous Condition”

# Table 5:  Non-Storm Water Discharge Assessment

# Table 6:  Failure to Certify Non-Storm Water Discharges

# Table 7:  Site Evaluation Summary

# Table 8:  BMP - Good Housekeeping Practices

# Table 9:  Preventive Maintenance

# Table 10:  Visual Inspection

# Table 11:  Spill Prevention and Response

# Table 12. Sediment and Erosion Control

# Table 13:  Runoff Control – Diversion Practices

# Table 14:  Runoff Control – Containment

# Table 15:  Other Controls

# Table 16:  BMP’s From Site Evaluation

# Table 17:  Employee Training Program

# Table 18:  Annual Site Compliance Evaluation

# Text boxes

http://iwrc.org/index.cfm/regulatory-summaries/

Iowa Waste Reduction Center, University of Northern Iowa